Implementation of a Portable Wireless Sensor Network Interface
Matt Buland, Marc Rubin, Tracy Camp

Abstract/Introduction
With many wireless sensor network deployments, there is often difficulty in assessing the current state of a network located in a remote location. During development, it's acceptable to have a large amount of equipment that takes up lots of space, but the opposite is true when traveling out to a deployment. The least amount of gear possible that will get the job done is generally desired. In an effort to reduce the amount of required equipment, a general purpose network interface will be developed to allow the user to monitor and communicate with their network. The target network will be an avalanche detection network that uses Xbee radios for communication.

Previous Work
This project does not have to start from scratch. Specifically, SparkFun has developed an arduino-esk board that can be programmed and used with an android device. Since it's portabile and versatile, the android platform makes for an excellent starting place. The board from sparkfun is called the IOIO-OTG. It's connected to via a TCP socket over USB, and contains a wide variety of analog and digital pins, allowing for lots of usability by a developer. Specifically for this project, the use of UART communication across any two compatible pins is of extreme use with Xbee radios.

Implementation